## Slide 1: Introduction To Eagle (and PCBs)

## Slide 2: PCBs are Made of Layers
Silkscreen – documentation labels
Metal – for making wires
Dialectric – insulation and structure
Solder mask – protective outer coating

## Slide 3: Metal Layers
The Metal layers
  Conductive “traces” to connect components
  Attaching components
More layers -> more expensive
Top and bottom layers are for mounting components and routing traces
Internal layers can serve several purposes
  Ground and power planes
  Other signal planes
  Internal routing layers

## Slide 4: Metal Layers (cont.)
Thickness is measured in oz per square foot.
Standard copper is 1oz
  About 0.034 mm

## Slide 5: Dielectric
The dielectric in the insulator between metal layers
Most PCBs use FR4
  “glass reinforced epoxy laminate”
  i.e., fancy fiberglass
  “FR” means “flame retardant”
Other specialized dielectrics are are available
  To support high speed circuits
  To manage thermal expansion

## Slide 6: Solder Mask
Plastic coating on the top and bottom of the board
Protects the top and bottom metal from oxidation.
Helps prevent solder bridges
Gives the board color
  FR4 is brown
  Solder mask comes in several colors.

## Slide 7: Silkscreen
It’s an opaque, (usually) white epoxy or polymer
It provides documentation and markings
  References designators
  Part outlines
  Logos
  Serial numbers etc.

## Slide 8: Lots of Choices, in Theory
There are many, many choices when designing a PCB
We will get to make very few of them
Cheap, fast PCB manufacturers provide a standard setup. E.g.:
  FR4
  1oz copper
  2, 4, or 6 layers
  A few colors

## Slide 9: Making Connections Between Layers
Plated holes connect metal layers.
Drill a hole
Electroplate it with copper
Cover it with a non-corroding metal.

## Slide 10: Throughholes and Vias
Through hole pads
  Mount devices with pins
  Sized for the pin + solder
  Always plated with non-oxidizing metal.
Vias are electrical connections
  As small as possible
Problems
  Takes up space in all layers
  Throughhole pins are generally pretty big
  Pin-to-pin spacing >= 1mm

## Slide 11: Surface Mount Devices (SMD)
No drill required
No pins
Smaller parts
Finer ‘pitch’ (pin-to-pin distance)
Parts on both sides
Easier automated placement
Pitch >= ~0.3 mm

## Slide 12: Eagle uses odd terminology
”Pads” are through hole connections
SMD (surface mount device) are surface mount connections.

## Slide 13: Designing PCBs

## Slide 14: Steps for Designing PCBs
Create/acquire a library of components
Assemble your schematic
Lay out the board
Perform design checks
Generate CAM files
Check them carefully
Submit for manufacturing

## Slide 15: PCB Library
One Symbol
Many Packages
Many Parts

## Slide 16: The Library
Package
Symbol
Device Pin Mapping
Physical part

## Slide 17: Schematics

## Slide 18: Layout

## Slide 19: Schematic vs. Board

## Slide 20: Designing with Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 22: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 23: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 24: Manufacturing
Eagle layers are partly Eagle-specific
  Some are semantic
  Some are documentary
Boards manufactures need
  Metal layers
  Silkscreen
  Soldermask
  Drills
  In a standard format

## Slide 25: Computer Aided Manufacturing (CAM) Files: Gerbers
Eagle’s CAM processor generates CAM files
  “Gerbers”
  “Drill file”
Manufacturing Reqs
  Minimum drill size
  Minimum feature width
  File formats
  Our manufacturer: https://jlcpcb.com/capabilities/Capabilities
Our configuration encodes their requirements
  QuadClass-Resources/Eagle/DRU/jlcpcb-4layer-5mil-small-cream.dru
  QuadClass-Resources/Eagle/CAM/jlcpcb-4layer-values-eagle9.cam

## Slide 26: The Lab
Use Eagle to design a simple schematic and board.
Run it through the tool flow.
Submit it through Eaglint

## Slide 27: Eagle Lint
lint:
  Tool to check coding standards and other invariants about a system.
Eaglint will check your libraries, schematics
  Check for correctness
  Check for style
Also checks for other files in your repo
  Eaglint will tell you what it’s looking for.
  Pay attention.
Provides a workflow for me to review your designs and provide feedback.
To use
  Visit http://eaglint.nvsl.io
  You received a welcome email a couple of nights ago.

## Slide 28: Eagle Lint Process
Commit and push your changes to github
Submit your repo to Eaglint for a quick check
Submit your repo to Eaglint for a full check
If warnings/errors
  Fix and goto 1.
Submit for human review
If rejected
  Read comments; goto 1.
Else if accepted
  Goto next lab

## Slide 29: Grading on PCB Labs
The key to PCB design is attention to detail.
  Building a real board can take 4 months.
  If you make a mistake, it takes 4 months to fix.
    Contrast to software: just recompile and rerun!
  Don’t make any mistakes! Check your work!
Grading for PCB labs
  A “perfect” score is 10 points
  You start out with 11-12 points (depending on the lab).
  Every time you submit a design to Eaglint, you lose 1 point.
  Every time you submit a design for human review Eaglint, you lose 1 point.
  You must complete the labs.
“Quick checks” are free.

## Slide 30: Next time:
Major points of confusion in this lab
  How to set and align to grid
  How to make wires straight
  Where to look for the SMD location in the button datasheet
  Adafruit tutorial is not consistent with our guidance

## Slide 31: Resources
Good PCB manufacturing videos
  https://www.youtube.com/playlist?list=PL8zP8UuDk8a0ZNWiteC-7PHx1HCeBY0qB