## Slide 1: Laying Out the Board

## Slide 2: Board Layout Goals
Mechanical constraints – Some things need to be in specific locations
Electrical constraints – Does the layout meet signal integrity/EM requirements
  Will digital interference mess up the antenna?
  Are decoupling caps near IC Supply pins?
  Keep the noisy power/ground for the motors away from the digital logic.
Correctness – things don’t overlap or hang off the board.
Ease of routing – Connected items should be physically close.
Make it pretty – you want a nice looking board
Potentially other, design-specific requirements

## Slide 3: Layout Steps
Define board shape.
Place mechanically important parts.
Define power planes
Place other parts
Route the board
Run DRC

## Slide 4: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 5: Device Placement: Style
Put all your components on a 1mm grid
Reference designators can go on 0.5 or 0.1mm grid.
Orient all your parts the same way for easy assembly.
Leave space between components for easy assembly.

## Slide 6: Layout Demo
Use the remote

## Slide 7: Eagle Layout Tools
You can rotate components with the rotate tool.
Control-click snaps parts to grid.

## Slide 8: Routing

## Slide 9: The Three Ways to Route
Manual
  You can do anything you want (including things you shouldn’t)
Auto router
  Fully-automatic routing, subject to constraints that you can set.
  The Eagle auto router is not good enough to do it all for you.
“Follow me”
  Assisted manual routing. The router will enforce the constraints you set.
Fan out
  Create circuit stubs to connect devices to power/ground

## Slide 10: Auto Router
Mixed reputation
  It can’t do everything
  Sometimes it does a bad job
  When it works, it’s great.
  Usually it needs some touch up.
Net classes (“Edit->Net Classes…”)
  Lets you set widths and clearances for different kinds of nets

## Slide 11: Semi-Automatic Routing
Route critical nets with follow me router
  Wires to antenna
  Wires to crystal
  Ground isolation for antenna and crystal
Fan out power and ground.
Autoroute everything else.

## Slide 12: Commands for Routing
“Auto;” – run the auto router (leave off the “;” to configure the router.
“Ripup;” – unroute signals
“Show <thing>” – Highlight a net or part

## Slide 13: Design Rules Check
Checks that your board layout meets design requirements for manufacturing.
  Distance between traces and traces, traces and vias, etc.
  Trace width
  Etc.

## Slide 14: Electrical Rules Check
This checks for common problems in schematics.
Make sure you understand the reason for the errors.
Fix them if you can.
Run it!

## Slide 15: Semi-Auto Routing Demo

## Slide 16: Routing and Layout Examples

## Slide 17: High-current Via
Via diameter matches trace width

## Slide 18: Battery to Jumper

## Slide 19: CAM Files

## Slide 20: CAM Layers (Gerber files)
Eagle layers are for design.
CAM layers are for manufacturing
  “Gerber” files are for lithographic steps
  Drill files are for drilling holes.
Each CAM layers corresponds to one layer of the resulting board
  Top silk screen (.PLC)
  Top solder mask (.STC)
  Top metal (.TOP)
  Inner metal layers
  Bottom metal (.BOT)
  Bottom solder mask (.STS)
  Bottom silk screen (.PLS)
  Different board houses have different suffixes.
One drill file specifying where all the pads, vias, and mounting holes are located and their diameters (.DRD)
Other files too, depending on the manufacturing process
  Solder paste stencil
  Assembly drawings

## Slide 21: The CAM Processor
The CAM Processor generates CAM files
The exact configuration for the gerber files varies by board house
  Should the board outline be in every layer?
  Which format should the files be in (there are many)
  Should the back side layers be mirrored?

## Slide 22: CAM Setup
To prepare Gerbers for a particular board house, you need CAM setup files (*.cam for Eagle)
This specifies how to generate each layer the board house needs.
See example in Button and Light Tutorial.

## Slide 23: CAM Demo

## Slide 24: Checking Your Gerbers!
Eagle can’t display Gerber files itself
You need a 3rd party tool
  See the Button and Light tutorial for recommendations
You should always check your Gerbers!
  Eagle has bugs (you should assume)
  You may have misconfigured something
  You may have put something in the wrong layer.

## Slide 25: Gerber Viewer Demo

## Slide 26: Quad Design Details

## Slide 27: Motor Power: Resistance
Motors take a lot of current!
We want all the power to go to the motors
Copper is an imperfect conductor
  Voltage drop on power lines is non-trivial
  Resistance is a function of aspect ratio
  0.5 mΩ/square
So, make the power lines wide!
  Use a trace-width calculator
  https://www.4pcb.com/trace-width-calculator.html

## Slide 28: Next Time
These slides need significant improvement.
Talk about placement of decoupling caps.
Update tips and tricks
Put more screen shots in to show how things should be laid out.
Discuss differential pairs
Had about 20 min of questions about previous labs
Then, demoed for about 1.5 hours.
Didn’t get past slide the “layout demo” slide

## Slide 29: Part Placement Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 30: Power Planes Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 31: Net Classes and Routing Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 32: Silkscreen Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 33: CAM File Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu